Project Overview
TGS5342 Carbon Monoxide Sensor
Carbon Monoxide Detector (Marine)
Reference Circuit
Safety Certifications

---
System Diagram
Generic Data Acquisition System
Sensor
Analog
Signal
Processing
Digital
Processing
Data
Storage
Logic
Comms /
Network
Interface
Human
Interface
(HMI)
ADC

---
System Diagram
CO Detector Black Box
Alarm Horn
Greatest of:
15dB above average
5dB above maximum
75dB
(NFPA 72)
LED
Status & operation
confirmation
Air Intake
30-69 ppm: 30 day alarm
70-149 ppm: 1-4 hour alarm
150-399 ppm: 10-50 min alarm
400+ ppm: < 4 min alarm
(UL)
Button
Silence & test

---
System Diagram
CO Detector System Diagram
Power
(Battery)
Microcontroller
CO
Sensor
Analog
Processing
Digital
Processing
Data
Storage
Logic
Serial
(RS-485)
Button
LED
Alarm
Horn
ADC

---
Analog Signal Processing
CO Sensor Circuit
R
+
-
Sensor Equivalent Circuit
Simple Single-Ended Op-Amp Circuit

---
Negative Feedback
Feedback
Network
Amplification
Σ
Input
Output

---
Negative Feedback
Feedback
Network
Amplification
Σ
Input
Output

---
Negative Feedback
Feedback
Network
Amplification
Σ
Input
Output

---
Negative Feedback
Rf
Σ
=
Input
Rin
Output

---
Negative Feedback
Rf
Σ
=
Input
Rin
Output

---
Negative Feedback
Rf
Σ
=
Input
Rin
Output

---
Signal Path Implementation
CO
Sensor
Sensor Circuit
Instrumentation Amplifier
Anti-aliasing Filter
Cypress PSoC1
100k
ADC

---
Signal Path Implementation Improvements
CO
Sensor
VREF
AGND
Sensor Circuit
Guard Traces
Bias Current Path
AGND
Anti-aliasing Filter
Corrected Values
Instrumentation Amplifier
MCU
?
ADC
?

---
Signal Path Implementation Improvements
Guarded Traces
Example In-Amp with Guarded Inputs
Image: https://www.ti.com/lit/ds/sbos034/sbos034.pdf?ts=1588264952402

---
Signal Path Implementation Improvements
Analog Ground Plane
Image: https://www.teledyne-e2v.com/content/uploads/2014/09/Board-Layout.pdf
Image: https://www.analog.com/media/en/training-seminars/design-handbooks/designers-guide-instrument-amps-chI.pdf
Decoupling Caps with Complimentary Frequency Response
Isolation of Analog and Digital Ground Return Current

---
Non-Ideal Capacitors
Images: https://www.analog.com/en/analog-dialogue/studentzone/studentzone-may-2017.html
Capacitor Frequency Response
Actual Capacitor Equivalent Circuit