Project Overview
CO Detector

---
Project Overview
TGS5342 Carbon Monoxide Sensor
Carbon Monoxide Detector (Marine)
Reference Circuit
Safety Certifications

---
System Diagram

---
System Diagram
Generic Data Acquisition System
Sensor
Analog
Signal
Processing
Digital
Signal
Processing
Data
Storage
Logic
Comms /
Network
Interface
Human
Interface
(HMI)
ADC

---
System Diagram
CO Detector Black Box
Alarm Horn
Greatest of:
15dB above average
5dB above maximum
75dB
(NFPA 72)
LED
Status & operation
confirmation
Air Intake
30-69 ppm: 30 day alarm
70-149 ppm: 1-4 hour alarm
150-399 ppm: 10-50 min alarm
400+ ppm: < 4 min alarm
(UL)
Button
Silence & test

---
System Diagram
CO Detector System Diagram
Power
(Battery)
Microcontroller
CO
Sensor
Analog
Signal
Processing
Digital
Signal
Processing
Data
Storage
Logic
Serial
(RS-485)
Button
LED
Alarm
Horn
ADC

---
Analog Signal Processing

---
Analog Signal Processing
CO Sensor Circuit
R
+
-
Sensor Equivalent Circuit
Simple Single-Ended Op-Amp Circuit

---
Analog Signal Processing
Negative Feedback
Feedback
Network
-
+
Amplification
Σ
Input
Signal
Output
Signal

---
Analog Signal Processing
Negative Feedback
Feedback
Network
-
+
Amplification
Σ
Input
Signal
Output
Signal

---
Analog Signal Processing
Negative Feedback
Feedback
Network
-
+
Amplification
Σ
Input
Signal
Output
Signal

---
Analog Signal Processing
Negative Feedback
Rf
Σ
=
Input
Signal
-
Rin
Output
Signal
+

---
Analog Signal Processing
Negative Feedback
Rf
Σ
=
Input
Signal
-
Rin
Output
Signal
+

---
Analog Signal Processing
Negative Feedback
Rf
Σ
=
Input
Signal
-
Rin
Output
Signal
+

---
Analog Signal Processing
Signal Path Implementation
+
-
-
CO
Sensor
+
-
+
Sensor Circuit
Instrumentation Amplifier
Anti-aliasing Filter
Cypress PSoC1
100k
ADC

---
Analog Signal Processing
Signal Path Implementation Improvements
+
-
-
CO
Sensor
+
-
+
VREF
AGND
Sensor Circuit
Guard Traces
Bias Current Path
AGND
Anti-aliasing Filter
Corrected Values
Instrumentation Amplifier
MCU
ADC

---
Analog Signal Processing
Signal Path Implementation Improvements
Guarded Traces
Example In-Amp with Guarded Inputs
Image: https://www.ti.com/lit/ds/sbos034/sbos034.pdf?ts=1588264952402

---
Analog Signal Processing
Signal Path Implementation Improvements
Analog Ground Plane
Image: https://www.teledyne-e2v.com/content/uploads/2014/09/Board-Layout.pdf
Image: https://www.analog.com/media/en/training-seminars/design-handbooks/designers-guide-instrument-amps-chI.pdf
Decoupling Caps with Complimentary Frequency Response
Isolation of Analog and Digital Ground Return Current

---
Analog Signal Processing
Non-Ideal Capacitors
Images: https://www.analog.com/en/analog-dialogue/studentzone/studentzone-may-2017.html
Capacitor Frequency Response
Actual Capacitor Equivalent Circuit

---
Analog Signal Processing
Signal Path Implementation Improvements
Self Test
nA
Current
Source
Instrumentation
Amplifier
CO
Sensor
Sensor Circuit
Mechanical relay enables connection to self-test current source.

---
ADC

---
ADC
Physical Restrictions
Cypress PSoC1 CY8C24223A
DELSIG8 8-Bit Delta Sigma ADC
6mA
25uA
Time [s]
MCU Active vs. Sleep Periods
Current [A]

---
ADC
Physical Restriction: Power
Restriction	Value	Units
Energy capacity of two AA batteries	7.8	Wh
Energy capacity of two AA batteries (90% efficiency)	7.0	Wh
Current capacity at 3.3V	2.1	Ah
MCU current draw while active	6.0	mA
MCU current draw while in sleep	25	uA
Minimum interval between battery replacements	1	year
Max seconds with MCU active	1.15E+06	sec
Min seconds with MCU in sleep	30.39E+06	sec
Percent active	3.6	%
6mA
25uA
Time [s]
MCU Active vs. Sleep Periods
Current [A]

---
ADC
Physical Restriction: Time
Restriction	Value	Units
Minimum ADC sample conversion time	31.25	us
Minimum MCU wake + sample time (estimated)	100	us
Sleep time (from ratio)	2.74	ms
Minimum sample interval time (100us + 2.74ms)	2.75	ms
Maximum sample rate	352	Hz
6mA
25uA
Time [s]
MCU Active vs. Sleep Periods
Current [A]

---
ADC
Sampling Rate & Nyquist-Shannon Theorem

---
ADC
Frequency Aliasing
Entire signal spectrum
Signal band of Interest
frequency
{f_s} over {2}
{f_s}
Amplitude

---
ADC
Frequency Aliasing
Entire signal spectrum
Signal band of Interest
frequency
{f_s} over {2}
{f_s}
Aliased frequencies
Amplitude

---
ADC
Frequency Aliasing
Low-pass filtering
Signal band of Interest
frequency
{f_s} over {2}
{f_s}
Amplitude

---
ADC
Frequency Aliasing
Low-pass filtering
Signal band of interest
frequency
{f_s} over {2}
{f_s}
Aliased frequencies
Amplitude

---
ADC
Frequency Aliasing
Low-pass filtering
Signal band of interest
frequency
{f_s} over {2}
{f_s}
Aliased frequencies
Amplitude

---
ADC
Anti-Aliasing Option 1: Precision Analog
High-order analog “anti-aliasing” filter before ADC
{f_s} over {2}
{f_s}

---
ADC
Anti-Aliasing Option 2: Oversampling
Low-order analog “anti-aliasing” filter before ADC
{f_s} over {2}
{f_s}
High-order digital filter after ADC

---
ADC
Signal Band of Interest
Decay time-constant for stable sensor reading:
τ ≈ 10 seconds
f ≈ 0.1 Hz
Image: https://www.figaro.co.jp/en/product/docs/tgs5141-p00_technical%20infomation%28en%29_rev05.pdf
Sensor Curves from Datasheet

---
ADC
Physical Restriction: Resolution
Restriction	Value	Units
ADC bit resolution	8	bit
Band of interest	0.3	Hz
Maximum sample frequency	352	Hz
Percent size of least significant bit (1 / 2^8)	0.39	%
Amplitude of least significant bit	-48	dB
100k
1uF
Vin
Vout
-48 dB
0.3 Hz
{f_s} over {2}

---
Digital Signal Processing

---
Digital Signal Processing
FIR vs. IIR Filters
Finite Impulse Response (FIR)
Function of input only: unconditionally stable.
High-order FIR filters require large number of taps.
Introduces larger phase delay than IIR filter.
Infinite Impulse Response (IIR)
Function of both input and output; can be unstable.
High-order FIR filter requires low number of taps.

---
Digital Signal Processing
FIR Filter
y[n] = {1} over {4} x[n] + {1} over {4} x[n-1] + {1} over {4} x[n-2] + {1} over {4} x[n-3]
Moving Average Filter
Simplest FIR filter.
Flat time-domain response.
Image:https://ptolemy.berkeley.edu/eecs20/week12/freqResponseRA.html
Windowed Sinc Filter
Coefficients of a sinc function scaled by a window function.
Image: https://tomroelandts.com/articles/how-to-create-a-simple-low-pass-filter

---
Logic Implementation

---
Logic Implementation
CO Detector Algorithm
RST
INIT
SENSOR
SELF TEST
SOUND
TEST
SENSOR
MALFUNC
SAMPLE
SLEEP
LOW
BATTERY
ALARM
ALARM
SILENCED
Image: https://gaslab.com/blogs/articles/carbon-monoxide-levels-chart
button
threshold
button

---
Review & Questions