Project Overview
CO Detector

---
Project Overview
TGS5342 Carbon Monoxide Sensor
Carbon Monoxide Detector (Marine)
Reference Circuit
Safety Certifications

---
System Diagram

---
System Diagram
Generic Data Acquisition System
Sensor
Analog
Signal
Processing
Digital
Signal
Processing
Data
Storage
Logic
Comms /
Network
Interface
Human
Interface
(HMI)
ADC

---
System Diagram
CO Detector Black Box
Alarm Horn
Greatest of:
15dB above average
5dB above maximum
75dB
(NFPA 72)
LED
Status & operation
confirmation
Air Intake
30-69 ppm: 30 day alarm
70-149 ppm: 1-4 hour alarm
150-399 ppm: 10-50 min alarm
400+ ppm: < 4 min alarm
(UL)
Button
Silence & test

---
System Diagram
CO Detector System Diagram
Power
(Battery)
Microcontroller
CO
Sensor
Analog
Signal
Processing
Digital
Signal
Processing
Data
Storage
Logic
Serial
(RS-485)
Button
LED
Alarm
Horn

---
Analog Signal Processing

---
Analog Signal Processing
CO Sensor Circuit
R
+
-
Sensor Equivalent Circuit
Simple Single-Ended Op-Amp Circuit

---
Analog Signal Processing
Negative Feedback
Feedback
Network
-
+
Amplification
Σ
Input
Signal
Output
Signal

---
Analog Signal Processing
Negative Feedback
Feedback
Network
-
+
Amplification
Σ
Input
Signal
Output
Signal

---
Analog Signal Processing
Negative Feedback
Feedback
Network
-
+
Amplification
Σ
Input
Signal
Output
Signal

---
Analog Signal Processing
Negative Feedback
Rf
Σ
=
Input
Signal
-
Rin
Output
Signal
+

---
Analog Signal Processing
Negative Feedback
Rf
Σ
=
Input
Signal
-
Rin
Output
Signal
+

---
Analog Signal Processing
Negative Feedback
Rf
Σ
=
Input
Signal
-
Rin
Output
Signal
+

---
Analog Signal Processing
Signal Path Implementation
+
-
-
CO
Sensor
+
-
+
Sensor Circuit
Instrumentation Amplifier
Anti-aliasing Filter
Cypress PSoC1
100k

---
Analog Signal Processing
Signal Path Implementation Improvements
+
-
-
CO
Sensor
+
-
+
VREF
AGND
Sensor Circuit
Guard Traces
Bias Current Path
AGND
Anti-aliasing Filter
Corrected Values
Instrumentation Amplifier
MCU
?
?

---
Analog Signal Processing
Signal Path Implementation Improvements
Guarded Traces
Example In-Amp with Guarded Inputs
Image: https://www.ti.com/lit/ds/sbos034/sbos034.pdf?ts=1588264952402

---
Analog Signal Processing
Signal Path Implementation Improvements
Analog Ground Plane
Image: https://www.teledyne-e2v.com/content/uploads/2014/09/Board-Layout.pdf
Image: https://www.analog.com/media/en/training-seminars/design-handbooks/designers-guide-instrument-amps-chI.pdf
Decoupling Caps with Complimentary Frequency Response
Isolation of Analog and Digital Ground Return Current

---
Analog Signal Processing
Non-Ideal Capacitors
Images: https://www.analog.com/en/analog-dialogue/studentzone/studentzone-may-2017.html
Capacitor Frequency Response
Actual Capacitor Equivalent Circuit

---
Analog Signal Processing
Signal Path Implementation Improvements
Self Test

---
Physical Restrictions
Cypress PSoC1 CY8C24223A
DELSIG8 8-Bit Delta Sigma ADC
6mA
25uA
Time [s]
MCU Active vs. Sleep Periods
Current [A]

---
Physical Restriction: Power
Restriction	Value	Units
Energy capacity of two AA batteries	7.8	Wh
Energy capacity of two AA batteries (90% efficiency)	7.0	Wh
Current capacity at 3.3V	2.1	Ah
MCU current draw while active	6.0	mA
MCU current draw while in sleep	25	uA
Minimum interval between battery replacements	1	year
Max seconds with MCU active	1.15E+06	sec
Min seconds with MCU in sleep	30.39E+06	sec
Ratio of active to sleep	36	%
6mA
25uA
Time [s]
MCU Active vs. Sleep Periods
Current [A]

---
Physical Restriction: Time
Restriction	Value	Units
Minimum ADC sample conversion time	31.25	us
Minimum MCU wake + sample time (estimated)	100	us
Sleep time (from ratio)	2.74	ms
Minimum sample interval time (100us + 2.74ms)	2.75	ms
Maximum sample rate	352	Hz
6mA
25uA
Time [s]
MCU Active vs. Sleep Periods
Current [A]

---
Sampling Rate & Nyquist-Shannon Theorem

---
Oversampling & Aliased Frequencies
Entire signal band and background noise
Signal band of Interest
frequency
{f_s}
Amplitude

---
Oversampling & Aliased Frequencies
Entire signal band and background noise
Signal band of Interest
frequency
{f_s} over {2}
{f_s}
Aliased frequencies
Amplitude

---
Oversampling & Aliased Frequencies
Low-pass filtering
Signal band of Interest
frequency
{f_s}
Amplitude

---
Oversampling & Aliased Frequencies
Low-pass filtering
Signal band of interest
frequency
{f_s} over {2}
{f_s}
Aliased frequencies
Amplitude

---
Oversampling & Aliased Frequencies
Low-pass filtering
Signal band of interest
frequency
{f_s} over {2}
{f_s}
Aliased frequencies
Amplitude

---
Physical Restriction: Resolution
Restriction	Value	Units
ADC bit resolution	8	bit
Percent size of least significant bit (1 / 2^8)	0.39	%
Attenuation at least significant bit	-48	dB
6mA
25uA
Time [s]
MCU Active vs. Sleep Periods
Current [A]

---
Designing a 1-Pole Anti-Aliasing Filter
2M
100uF
Vin
Vout